## Slide 1
CNN IP Controller
청주대학교 장 경 석

## Slide 2
Contents
1. Outline & IP Design Plan
2. FSM Design Plan
3. Block Diagram & Flow Chart
4. Timing Diagram

## Slide 3
Convolution Controller
Design Plan
Condition
1) Assumed ARM Interface code and BRAM data are already existed.
2) Input data and Weight data are changed 32bit floating point to 16bit fixed point.
3) Using three block memories.
4) Need to consider kernel size, stride, padding
- Kernel size defines the number of PE modules.
- Stride defines kernel’s movement in PE modules.
- Padding defines edge data of input.
How to consider kernel, stride, padding?
1) Kernel
Kernel size defines the number of PE modules. If using 3x3 filter, the number of filter is 9, using 5x5 filter, the number of filter is 25.
2) Stride
We will use shift register for considering stride.
PE
S
W
I
Mult
Shift Register
Image
Weight
Read 5 col of weight
Read 4 col of image
For(x < image_width)
Read 1 col of image
Do MAC
Write Result

## Slide 4
Design Plan
Address Map
How to consider kernel, stride, padding?
3) Padding
If(count % (224+(padding*2))>224+padding
If(count / (224+(padding*2))<padding
If(count / (224+(padding*2))>224+padding
If(count % (224+(padding*2))<padding
Inner Register
Input
Weight
Conv
Reserved
Reserved
Reserved
Signal 1
Signal 2
Signal 3
Signal 4
0x43C00000
0x43C00004
0x43C00008
0x43C0000C
0x43C00100
0x43C0C400
0x43C0C500
0x43C0C5F0
0x43C0C700
0x43C18B00

## Slide 5
Finite State Machine (IDLE)
Definition of each signal properties
1) Start signal
2) Input Done signal
3) Weight Done signal
4) Convolution Done signal
5) Write Done signal
IDLE state properties
When Finite State Machine starts, First state is IDLE, means waiting next state signal and doing nothing. If Start signal goes high level, state will be next stage, READ.
Finite State Machine (READ)
Read State properties
When Start signal is high level, Read state begins. In Read state, Finite State Machine send enable signal and specific address to BRAM_Input and BRAM_Weight. It will read input data and weight data that is sent by ARM Interface. When all of input data is read, it will send Input Done signal, 1. and when all of weight data is read, it will send Weight Done signal, 1. If Input Done signal data is 1 and Weight Done signal data is 1, Read state will be done.
IDLE
READ
Start
READ
If(Addr == (Input Size))
I_Done == 1
If(Addr == (Weight Size))
W_Done == 1
I_Done == 1 && W_Done == 1

## Slide 6
Finite State Machine (CONV)
Convolution State properties
When I_Done & W_Done signal are high level, convolution state begins. If convolution state begin, Input data multiplies to Weight data in PE module. That data will be sum data and output of PE module. Output data will be calculated lots of PE modules. If We choose 3x3 Filter, the number of PE modules is 9, and choose 5x5 Filter, the number of PE modules is 25. When convolution state is done, convolution_Done signal goes high level.
Finite State Machine (WRITE)
Write State properties
When Convolution_Done signal is high level, Write state begins. If Write state begin, convolution result data will be written and saved in BRAM_Result Memory. When Write state is done(that means all of convolution result data are written and saved in BRAM_Result Memory), Write_Done signal goes high level and current state go back to IDLE state.
PE
S
W
I
PE
S
W
I
PE
S
W
I
Convolution Result Data in
Write Done = 1
BRAM
Address Map
Result
Reserved
Signal 1
Signal 2
Signal 3
Signal 4

## Slide 7
BRAM
Address Map
Input
Controller
IDLE
R
W
C
(PE)
BRAM
Address Map
Weight
BRAM
Address Map
Result
Inner Register
Input
Weight
Conv
Reserved
Reserved
Reserved
Signal 1
Signal 2
Signal 3
Signal 4
How to Design ( Connect BRAM & Controller & Convolution Module & No Arbiter)
< CNN Controller >
Convolution (PE)
W
S
I

## Slide 8
How to Design
IDLE
If(I_Done &&W_Done)
( Flow Chart )
READ
Start
Input Data Read
Input Done = 1
Weight Done = 1
Weight Data Read
< Read State >
Conv (PE)
WRITE
BRAM
Address Map
Input
Reserved
Signal 1
Signal 2
Signal 3
Signal 4
BRAM
Address Map
Weight
Reserved
Signal 1
Signal 2
Signal 3
Signal 4

## Slide 9
How to Design
IDLE
(Flow Chart)
READ
< Convolution State >
Conv (PE)
If(C_Done == 1)
WRITE
Convolution (PE)
Input
Weight
Sum
Convolution_Done = 1
I
W
S
Input / Weight In

## Slide 10
How to Design
IDLE
If(W_Done == 1)
(Flow Chart)
READ
Start
< Write State >
Conv (PE)
If(C_Done == 1)
WRITE
Convolution Result Data in
Write Done = 1
BRAM
Address Map
Result
Reserved
Signal 1
Signal 2
Signal 3
Signal 4
If(Write_Done == 1)

## Slide 11
CLK
RSTn
cState
nState
Start
En_Input
Addr_Input
Input_Done
En_Weight
Addr_Weight
Weight_Done
Input_Reg
Weight_Reg
Conv_Reg
C_Done
En_Re
Wen_Re
Addr_Result
D_in_Result
Write_Done

## Slide 12
Thank you
청주대학교 장 경 석